## Slide 1: Triangulation Using Computer Vision
Cot5930: Introduction to Robotics
Dr. Ravi Shankar
By
Huajin Ariel Qu & Charles Perry Weinthal

## Slide 2: Overview
Four Raspberry Pi have been configured with USB WebCams to view the movement grid, these four units then report via WiFi connections to a main computational and control Unit. The main unit will then compute the distance using triangulation and command the Robot to move via a Bluetooth interface.

## Slide 3: Where is the Robot?
B()
d
c
b
a
(x,y)
Cameras are
located at
A, B, C, D
A()
C()
D ()

## Slide 4: Triangulation Formulas
For Camera A & C:
For Camera B & D:

## Slide 5: Current Camera View
A()
B()
C()
D ()
Cameras are
located at
A, B, C, D
Inside the arc is the linear zone.
The angles are the vision boundaries.

## Slide 6: Choose the Best Camera for Your Solution
Only a few cameras will be in position to satisfy:
= camera’s linear range

## Slide 7: Error Analysis
We generated the data to simulate the Distances and Angles given by four cameras;
The Robot locations were calculated by the formula given in previous slides;
The average errors were mapping in the following plot:

## Slide 8: The infinite number is the “blind spot”, as we assumed the longer the distance the bigger the error, locations that are closer to cameras get smaller errors.
Error Analysis, cont’d

## Slide 9: Error Analysis & Confidence in the Data Using MathLab:
% summerize:
C=[-1,-1,9,9,-1,9,9,-1]; %camera location
%actual distancen and angle with respect to four cameras
D=[a,b,c,d]
A=[angle1*180/pi,angle2*180/pi,angle3*180/pi,angle4*180/pi]
% add some error for the distance. the farther, the larger error
a_e=randi([-round(a),round(a)]);
b_e=randi([-round(b),round(b)]);
c_e=randi([-round(c),round(c)]);
d_e=randi([-round(d),round(d)]);
D_e=[a+0.01*a_e,b+0.01*b_e,c+0.01*c_e,d+0.01*d_e]
%estimated location from calculation:
x1=-1+D_e(1)*sind(A(1)); y1=-1+D_e(1)*cosd(A(1));
x2=-1+D_e(2)*cosd(A(2));y2=9-D_e(2)*sind(A(2));
x3=9-D_e(3)*sind(A(3));y3=9-D_e(3)*cosd(A(3));
x4=9-D_e(4)*cosd(A(4));y4=-1+D_e(4)*sind(A(4));
R_x=[x1,x2,x3,x4]
R_y=[y1,y2,y3,y4]
e_p=[sqrt((x1-R(1))^2+(y1-R(2))^2)/sqrt(R(1)^2+R(2)^2),sqrt((x2-R(1))^2+(y2-R(2))^2)/sqrt(R(1)^2+R(2)^2),sqrt((x3-R(1))^2+(y3-R(2))^2)/sqrt(R(1)^2+R(2)^2),sqrt((x4-R(1))^2+(y4-R(2))^2)/sqrt(R(1)^2+R(2)^2)]

## Slide 10: Error Analysis & Confidence in the Data Using MathLab:
Actual Robot Location: | x= | 4 | y= | 4
Camera Location: | A(-1,-1) | B(-1,9) | C(9,9) | D(9,-1)
Distance to robot: | 7.0711 | 7.0711 | 7.0711 | 7.0711
Angle: | 45 | 45 | 45 | 45
Distance with error: | 7.1111 | 7.1111 | 7.0211 | 7.0711
Estimated location x: | 4.0283 | 4.0283 | 4.0354 | 4
Estimated location y: | 4.0283 | 3.9717 | 4.0354 | 4
Error Percentage: | 0.18% | 0.35% | 0.53% | 0.71%
Averaged Error percent: | 0.44% |  |  | 

## Slide 11: Optimizing For the Best Results.
Only a few cameras will be in position to satisfy:
: < 1% error if D
For Camera A & C: : For Camera B & D:
Actual errors to be examined in detail later, per Dr. Shankar 15apr2015

## Slide 12: Proposed Camera View
A
()
B
()
C
()
D
()
Cameras are
located at
A, B, C, D
Inside the arc is the linear zone.
The angles are the vision boundaries.
Gap Exaggerated.

## Slide 13: Locations, Distances & Vectors
We generated a few test vectors to verify the triangulation code.

## Slide 14: Python Code
The code expects 4 vectors and yields the Cartesian coordinates:

## Slide 15: Credits & Acknowledgments
Photo Credits:
Santiago Aguerre
Caio Farias
Charles Weinthal
Huajin Qu